## Slide 1
Department of Computer Science and Engineering
EMBEDDED PROGRAMMING
ConcreSense: IoT-Based Concrete Quality Verification System
Supervisor: Dr. [Faculty Name], Dept. of CSE
Presentation by: [Student Name(s)] | [Roll No.] | [Year & Section]
EMBEDDED PROGRAMMING PROJECT-ZEROTH REVIEW

## Slide 2: CONTENTS
Introduction
Problem Statement
Project Description
Aim and Scope of the Proposed work
Literature Survey
Hardware Component
Block Diagram Design
Project Planning

## Slide 3: Introduction
Background
Concrete is the most widely used construction material worldwide, forming the backbone of infrastructure projects ranging from bridges and dams to residential buildings.
The Problem
Material fraud involving substandard or adulterated concrete is a persistent challenge in construction, leading to structural failures and safety hazards. Traditional quality testing methods are lab-based, slow, and easy to manipulate.
Our Solution: ConcreSense
ConcreSense is a low-cost, portable IoT device powered by the ESP32 microcontroller. It uses an array of sensors and an on-device TinyML model to instantly assess concrete quality at the construction site, GPS-tag each test, and push results to a secure cloud dashboard — making material fraud detectable in real time.
Key Technologies
ESP32 Microcontroller | TinyML (Edge Impulse SDK) | Sensor Fusion | NEO-6M GPS | MQTT / Wi-Fi | Cloud Dashboard

## Slide 4: Problem Statement
Construction quality fraud and the absence of real-time concrete verification pose serious risks to structural safety and public infrastructure. Existing solutions fail to provide immediate, tamper-proof, on-site testing at low cost.
Key Challenges
Delayed Testing: Conventional cube strength tests take 7 to 28 days in a laboratory, providing no real-time feedback during active pours.
Material Fraud: Substandard concrete — with incorrect water-cement ratios, added impurities, or inadequate mixing — is routinely supplied without detection.
No Location Traceability: Current inspection records lack GPS-verified timestamps, making it impossible to audit which batch was used at which site location.
High Equipment Cost: Professional concrete analyzers cost ₹50,000 to ₹5,00,000, making them inaccessible to small and mid-scale contractors.
Need
An affordable, embedded IoT system capable of real-time concrete quality classification, GPS tagging, and secure cloud reporting — deployable by any site engineer without laboratory infrastructure.

## Slide 5: Project Description
ConcreSense is a portable, battery-powered IoT device that performs instant on-site concrete quality verification using sensor fusion and TinyML inference — without any laboratory infrastructure.
How It Works
Sense: Multi-sensor array (load cell, moisture, temperature, accelerometer) captures fresh concrete properties in under 60 seconds.
Classify: On-device TinyML model (trained via Edge Impulse) classifies the batch as GOOD, MARGINAL, or REJECT based on IS 456:2000 parameters.
Tag: NEO-6M GPS module appends geographic coordinates and UTC timestamp to every test result.
Report: Results are shown on an OLED display and transmitted via Wi-Fi (MQTT) to a secure cloud dashboard with real-time alerts, test history maps, and PDF export.
Target Cost: Under ₹5,000 per unit | Target Classification Accuracy: ≥ 90%

## Slide 6: Aim and Scope of the Proposed work
Aim
To design, develop, and validate an embedded IoT system (ConcreSense) that performs real-time, on-site concrete quality verification using TinyML on the ESP32 and delivers GPS-tagged results to a secure cloud dashboard to detect and prevent material fraud in construction.
Scope of Work
Hardware: Integrate load cell, capacitive moisture, temperature, and vibration sensors with ESP32 and GPS module into a portable, IP-rated enclosure.
Machine Learning: Train and deploy a TinyML classification model on the ESP32 using Edge Impulse, targeting ≥ 90% accuracy across Good, Marginal, and Reject categories.
Cloud Integration: Build an MQTT-connected dashboard for real-time alerts, geo-mapped test history, and report export; compliant with IS 456:2000 quality benchmarks.
Future Scope
Ultrasonic pulse velocity testing for hardened concrete | Blockchain-backed immutable audit trail | Multi-site fleet management portal

## Slide 7: Literature Survey
[1] Nasr et al. (2021) — CNN for Concrete Crack Detection
Achieved ~92% accuracy detecting cracks using image-based CNNs. Limitation: only addresses hardened concrete defects; cannot assess fresh concrete quality or fraud.
[2] Cha et al. (2019) — Deep Learning for Structural Defect Detection
Demonstrated TinyML feasibility on ARM Cortex-M edge devices for structural monitoring. Validated that lightweight neural networks can run inference on microcontrollers at low power.
[3] ESP32-Based IoT for Construction Monitoring (2022)
Real-time temperature and humidity monitoring during concrete curing using ESP32. Useful precedent but limited to environmental parameters; no quality classification or fraud detection.
[4] Edge Impulse / TinyML Research (2023)
Sensor-fusion TinyML models for construction material classification on edge devices achieved 88% accuracy. Confirms viability of on-device inference without cloud dependency.
Research Gap
No existing system combines multi-sensor fusion, on-device TinyML classification, GPS traceability, and a secure cloud dashboard in a single affordable device for fresh concrete quality verification at the pour site.

## Slide 8: Hardware Component
ESP32 Development Board — Main microcontroller; dual-core 240 MHz, built-in Wi-Fi and Bluetooth, 520 KB SRAM for TinyML inference.
Load Cell + HX711 Amplifier — Measures compressive force and slump consistency of fresh concrete mix.
Capacitive Moisture Sensor (FC-28) — Detects water-cement ratio anomalies (excess water weakens concrete strength).
DS18B20 Temperature Sensor — Monitors concrete mix temperature; extreme temps affect curing and final strength.
MPU-6050 (Accelerometer / Gyroscope) — Captures vibration signatures during mixing to detect segregation or air voids.
NEO-6M GPS Module — Geo-tags every test with latitude, longitude, and UTC timestamp for audit traceability.
OLED Display (SSD1306, 0.96”) — On-device display of classification result (GOOD / MARGINAL / REJECT) for field engineer.
Li-Ion Battery Pack (3.7 V, 5000 mAh) + TP4056 Charger — Enables full-day field operation without mains power.
3D-Printed IP54-Rated Enclosure — Dust and splash resistant housing designed for rugged construction site conditions.

## Slide 9: Block Diagram Design
The ConcreSense system follows a three-layer IoT architecture — Sensing, Processing, and Communication — all hosted on the ESP32.
Layer 1 — Sensor Layer (Inputs)
Load Cell (HX711) → ESP32 GPIO | Moisture Sensor → ESP32 ADC | DS18B20 → OneWire Bus | MPU-6050 → I²C Bus | NEO-6M GPS → UART
Layer 2 — Processing Layer (ESP32 Core)
Raw sensor data is pre-processed (normalization, feature extraction) by ESP32 Core 0. Core 1 runs the TinyML inference engine (Edge Impulse SDK) to classify the batch as GOOD, MARGINAL, or REJECT. GPS coordinates and timestamp are appended to the result payload.
Layer 3 — Communication and Display Layer (Outputs)
OLED Display: Immediate on-screen result for field engineer. Wi-Fi / MQTT: JSON payload transmitted to cloud broker (e.g., HiveMQ / AWS IoT). Dashboard: React-based web portal renders live map, result history, trend charts, and PDF export. Alert System: Automated email / SMS alert on REJECT classification.
Full cycle — sensor read to cloud update: < 5 seconds

## Slide 10: Project Planning
The project is planned over 12 weeks from component procurement to final demonstration and documentation.
Week 1–2: Component Procurement and Hardware Setup
Source ESP32, sensors, GPS module, display, and enclosure materials. Verify component specifications and set up development environment (Arduino IDE / PlatformIO, Edge Impulse).
Week 3–4: Sensor Integration and Data Acquisition
Interface all sensors with ESP32. Validate data readings against known concrete mixes. Build data logging pipeline for ML dataset collection.
Week 5–6: Dataset Collection and Labelling
Prepare concrete batches of varying quality (correct mix, excess water, sand substitution). Collect 200+ labelled sensor readings across GOOD, MARGINAL, and REJECT classes.
Week 7–8: TinyML Model Training and Deployment
Train classification model on Edge Impulse. Optimize for ESP32 SRAM constraints. Deploy quantized model to ESP32 firmware and test inference accuracy on holdout data.
Week 9–10: GPS, Wi-Fi, Cloud Dashboard Integration
Integrate GPS module, implement MQTT transmission, and build cloud dashboard with map view, history log, alerts, and PDF export.
Week 11: Field Testing and Calibration
Conduct field trials at a simulated construction site. Calibrate sensors, validate GPS accuracy, and stress-test the enclosure. Cross-check results against IS 456:2000 benchmarks.
Week 12: Documentation and Final Review Presentation
Complete project report, circuit diagrams, and code documentation. Prepare and deliver final demonstration to review panel.